## Slide 1: 18ECC303J – Computer Communication Networks
Course Credit : 4
Theory : 9 Hours
Reference Text Books
1.Behrouz A. Fehrouzan, “Data communication & Networking”, Mc-Graw Hill, 5th Edition Reprint, 2014.
2. Andrew S. Tanenbaum, “Computer Networks”, Pearson Education India, 5th Edition, 2013.
3. William Stallings, “Data & Computer Communication”, Pearson Education India, 10th Edition, 2014.

## Slide 2: Unit 3 – Network Layer
Session 11
Routing Information Protocol-RIP
Session 12
Open Shortest Path First-OSPF
Session 13
Border Gateway Protocol-BGP
Week 9

## Slide 3: Unicast Routing Protocols: RIP, OSPF, and BGP
Objectives
Upon completion you will be able to:
Understand distance vector routing and RIP
Understand link state routing and OSPF
Understand path vector routing and BGP

## Slide 4: Session 11:RIP
The Routing Information Protocol (RIP) is an intradomain routing protocol used inside an autonomous system. It is a very simple protocol based on distance vector routing.
The topics discussed in this section include:
RIP Message Format Requests and Responses Timers in RIP
RIP Version 2 Encapsulation

## Slide 5: RIP
RIP: Routing Information Protocol
  Based on distance vector routing
Design considerations
  In a AS, RIP deals with routers and networks (links)
  The destination in a routing table is a network
    The first column defines a network address
  The metric used in RIP is hop count
  Infinity is defined as 16
    Any route in an AS cannot have more than 15 hops

## Slide 6: RIP Message Format
Command: 8-bit
  The type of message: request (1) or response (2)
Version: 8-bit
  Define the RIP version
Family: 16-bit
  Define the family of the protocol used
  TCP/IP: value is 2
Network Address: 14 bytes
  Defines the address of the destination network
  14 bytes for this field to be applicable to any protocol
  However, IP currently uses only 4 bytes, the rest are all 0s
Distance: 32-bit
  The hop count from the advertising router to the destination network

## Slide 7: RIP Message Format
igure 13-6 | 

## Slide 8: Requests and Response
RIP uses two type of messages
  Request and response
Request
  Sent by a router that has just come up or has some time-out entries
  Can ask specific entries or all entries

## Slide 9: Request Messages
F
igure 13-7 | 

## Slide 10: Requests and Response (Cont.)
Response: solicited or unsolicited
  A solicited response: sent only in answer to a request
    Contain information about the destination specified in the corresponding request
  An unsolicited response: sent periodically
    Every 30s
    Contains information about the entire routing table
    Also called update packet

## Slide 11: Figure : Example of a Domain Using RIP

## Slide 12: Review Question
Following Figure shows the update message sent from router R1 to router R2 in Fig given in the previous slide.
  The message is sent out of interface 130.10.0.2
The message is prepared with the combination of split horizon and poison reverse strategy in mind.
  Router R1 has obtained information about networks 195.2.4.0, 195.2.5.0, and 195.2.6.0 from router R2.
  When R1 sends an update message to R2,
 Replace the actual value of the hop counts for these three networks with 16 (infinity) to prevent any confusion for R2.
The figure also shows the table extracted from the message.
  Router R2 uses the source address of the IP datagram carrying the RIP message from R1 (130.10.02) as the next hop address.

## Slide 13
Solution

## Slide 14: Timers in RIP
RIP uses three timers
  Periodic timer
  Expiration timer
  Garbage collection timer

## Slide 15: RIP Timers
F
igure 13-10 | 

## Slide 16: Periodic Timer
Periodic timer
  Control the advertising of regular update message
  Although protocol specifies 30 s, the working model uses a random number between 25 and 35 s
 Prevent routers update simultaneously

## Slide 17: Expiration Timer
Govern the validity of a route
Set to 180 s for a route when a router receives update information for a route
  If a new update for the route is received, the timer is reset
  In normal operation, this occurs every 30 s
If timer goes off, the route is considered expired
  The hop count of the route is set to 16, which means
destination is unreachable

## Slide 18: Garbage Collection Timer
When a route becomes invalid, the router does not immediately purge that route from its table
It continues advertise the route with a metric value of 16
A garbage collection timer is set to 120 s for that route
When the count reaches zero, the route is purged from the table
Allow neighbors to become aware of the invalidity of a route prior to purging

## Slide 19: Review Question
A routing table has 20 entries.
It does not receive information about five routes for 200 seconds.
How many timers are running at this time?

## Slide 20: Solution
The timers are listed below:
  Periodic timer: 1
  Expiration timer: 20 - 5 = 15
  Garbage collection timer: 5

## Slide 21: RIP Version 2
Does not augment the length of the message of each entry
Only replace those fields in version 1 that were filled with 0s with some new fields

## Slide 22: RIP Version 2
New fields
  Routing Tag: carries information such as the autonomous system number
    Enable RIP to receive information from an exterior routing table
  Subnet mask: carries the subnet mask (or prefix)
    RIP2 support classless addressing and CIDR
  Next-hop address: show the address of the next hop

## Slide 23: RIP-v2 Format
F
igure 13-16

## Slide 24: Classless Addressing
The most important difference between the two versions
  classful v.s. classless addressing
RIPv1 uses classful addressing
  The only entry in the message format is the
network address (with a default mask)
RIPv2 support classless addressing
  Adds one filed for the subnet mask

## Slide 25: Authentication
Protect the message against unauthorized advertisement
The first entry of the message is set aside for authentication information
  Family field = FFFF16
    Not used for routing information but for authentication
  Authentication type
    Define the method used for authentication
  Authentication data
    Contain the actual authentication data

## Slide 26: Authentication
F
igure 13-17 | 

## Slide 27: Multicasting
Version 1 of RIP uses broadcasting to send RIP message to every neighbor
  All the routers and the hosts receive the packets
RIP version 2
  Uses the multicast address 224.0.0.9 to multicast RIP message only to RIP routers in the network

## Slide 28: Encapsulation
RIP message are encapsulated in UDP user datagram
The well-known port assigned to RIP in UDP is port 520

## Slide 29: Session:12 OSPF
The Open Shortest Path First (OSPF) protocol is an intradomain routing protocol based on link state routing. Its domain is also an autonomous system.
The topics discussed in this section include: Areas
Metric
Types of Links
OSPF Packets
Link State Update Packet Encapsulation

## Slide 30: Areas
OSPF divides an autonomous system into areas
  To handle routing efficiently and in a timely manner
A collection of networks, hosts, and routers all contained within an autonomous system
Thus, an autonomous system can be divided into many different areas
All networks inside an area must be connected

## Slide 31: Areas (Cont.)
Routers inside an area flood the area with
routing information
At the border of an area, special routers called
area border routers
  Summarize the information about the area and sent it to other areas

## Slide 32: Areas (Cont.)
Among the area inside an autonomous system is a special area called backbone
  All of the areas inside an AS must be connected to the backbone
The routers inside the backbone are called the
backbone routers
  A backbone router can also be an area border router

## Slide 33: Areas (Cont.)
If the connectivity between a backbone and an area is broken
  A virtual link must be created by the administration through alternate (lengthy) path
Each area has an area identification
  The area identification of the backbone is zero

## Slide 34: Areas in an Autonomous System
F
igure 13-18 | 

## Slide 35: Metrics
OSPF allows the administrator to assign a cost, called the metric, to each route
Metric can be based on a type of service
  Minimum delay
  Maximum throughput
A router can have multiple routing tables
  Each based on a different type of service

## Slide 36: Types of Links
In OSPF, a connection is called a link
Four types of links
  Point-to-point
  Transient
  Stub
  Virtual

## Slide 37: Types of Links
F
igure 13-19 | 

## Slide 38: Point-to-Point Link
Connect two routers without any other host or router in these two routers
Example
  Telephone line
  T-line
Graphically representation
  The routers are represented by nodes
  The link is represented by a bidirectional edge
The metric
  Usually the same at the two ends

## Slide 39: Point-to-Point Link
F
igure 13-20 | 

## Slide 40: Transient Link
A network with several routers attached to it
  Data can enter through any of the routers and leave through any router
Example
  All LANs and some WANs with two or more routers

## Slide 41: Transient Link (Cont.)
Graphically representation
  Figure b in the next slide. However, it is
    Not efficient: each router need to advertise the neighborhood of four other routers
      For a total of 20 advertisement
    Not realistic: there is no single network (link) between each pair of routers
      There should be only one network that serves as a crossroad between all five routers

## Slide 42: Transient Link (Cont.)
Reality: each router should be connected to every router through one single network
  The network is represented by a node
  However, network is not a machine
    Cannot function as a router
Solution: one of the routers acts as a single network
  This router has a dual purpose: a true router and a
designated router
    The link is represented as a bidirectional edge
    Figure c in the next slide

## Slide 43: Transient Link
F
igure 13-21 | 

## Slide 44: Stub Link
A network that is connected to only one router
  Data packet enter and leave through this only one router
A special case of transient network
Graphically representation
  The router as a node
  The designated router as the network
  Note, the link is only one-directional
    From the router to the network
    Because the network is the end point in the graph representation
      See the following third slides

## Slide 45: Stub Link
F
igure 13-22

## Slide 46: Virtual Link
When the link between two routers is broken
  The administrator may create a virtual path between them using a longer path and may go through several routers

## Slide 47
Figure
Example of an AS and its graphical representation in OSPF

## Slide 48: Types of Packets
OSPF uses five different packets
  Hello packet
  Database description packet
  Link state request packet
  Link state update packet
    Router link
    Network link
    Summary link to network
    Summary link to AS boundary router
    External link
  Link state acknowledgment packet

## Slide 49: Types of OSPF Packets
F
igure 13-33 | 

## Slide 50: Common Header
All OSPF packets share the same header
  Version: 8-bit
    The version of the OSPF protocol. Currently, it is 2
  Type: 8-bit
    The type of the packet
  Message length: 16-bit
    The length of the total message including the header
  Source router IP address: 32-bit
    The IP address of the router that sends the packet

## Slide 51: OSPF Common Header
F
igure 13-34 | 

## Slide 52: Common Header (Cont.)
Area identification: 32-bit
  The area within which the routing take place
Checksum: 16-bit
  Error detection on the entire packet excluding the authentication type and authentication data field
Authentication type: 16-bit
  Define the authentication method used in this area
  0: none, 1: password
Authentication: 64-bit
  The actual value of the authentication data
  Filled with 0 if type = 0; eight-character password if type = 1

## Slide 53: Hello Message
OSPF uses the hello message to
  Create neighborhood relationships
  Test the reachability of neighbors
First step in link state routing
  It must first greet its neighbors

## Slide 54: Hello Packet
F
igure 13-35

## Slide 55: Hello Packet Format
Network mask: 32-bit
  Define the network mask of the network over which the hello message is sent
Hello interval: 16-bit
  Define the number of seconds between hello message
E flag: 1-bit
  If it is set, the area is a stub area
T flag: 1-bit
  If it is set, the router supports multiple metrics

## Slide 56: Hello Packet Format (Cont.)
Priority
  The priority of the router. Used for the selection of the designated router
  The router with the highest priority is chosen as the designated router
  The router with the second highest priority is chosen as the backup designated router
  If it is 0, the router never wants to be a designated or backup designated router

## Slide 57: Hello Packet Format (Cont.)
Dead interval: 32-bit
  The number of seconds before a router assumes that a neighbor is dead
Designated router IP address: 32-bit
Backup designated router IP address: 32-bit
Neighbor IP address: a repeated 32-bit field
  A current list of all the neighbors from which the sending router has received the hello message

## Slide 58: Database Description Message
When a router is connected to the system for the first time or after a failure, it needs the complete link state database immediately
Thus, it sends hello packets to greet its neighbors
If this is the first time that the neighbors hear from the router, they send a database description packet

## Slide 59: Database Description Message (Cont.)
The database description message does not contain complete database information
  It only gives an outline, the title of each line in the database
The newly router examines the outline and find out which lines it does not have
  Send one or more link state request packets to get full information about that particular link
  The content of the database may be divided into several message

## Slide 60: Database Description Message (Cont.)
When two routers want to exchange database description packets
  One of them acts as master
  The other is the slave

## Slide 61: Database Description Packet
F
igure 13-36 | 

## Slide 62: Database Description Message Format
E flag: 1-bit
  Set to 1 if the advertising router is an autonomous boundary router
B flag: 1-bit
  Set to 1 if the advertising router is an area border router
I flag: 1-bit, the initialization flag
  Set to 1 if the message is the first message
M flag: 1-bit, more flag
  Set to 1 if this is not the last message

## Slide 63: Database Description Message Format (Cont.)
M/S flag: 1-bit, master/slave flag
  Indicate the origin of the packet. Master = 1, Slave = 0
Message sequence number: 32-bit
  Contain the sequence number of the message
LSA header: 20-bit
  Used in each LSA(Link State advertisement)
  The format of this header is discussed in the link state update message
 Only give the outline of each link
  It is repeated for each link in the link state database

## Slide 64: Link State Request Packet
Sent by a router that needs information about a specific route or routes
  Answered with a link state update packet
Used by a newly connected router to request more information after receiving the database description packet

## Slide 65: Link State Request Packet
F
igure 13-37 | 

## Slide 66: LSA Header (OSPF Update carries LSAs)

## Slide 67: LSA Header Fields
LS age—Time, in seconds, elapsed since the LSA was originated. An LSA ages in the LSDB (added by 1 per second), but does not age during transmission.
LS type—Type of the LSA.
Link state ID—The contents of this field depend on the LSA's type.
LS sequence number—Used by other routers to judge new and old LSAs.
LS checksum—Checksum of the LSA except the LS age field.
Length—Length in bytes of the LSA, including the LSA header.

## Slide 68: Link State Acknowledgment Packet
OSPF forces every router to acknowledge the receipt of every link state update packet
  Make routing more reliable
Format
  Common header
  Link state header

## Slide 69: Link State Acknowledgment Packet
F
igure 13-49

## Slide 70: Encapsulation
OSPF packets are encapsulated in IP datagram
  OSPF contains the acknowledgment mechanism for flow and error control
  Doe not need a transport layer protocol to provide these services

## Slide 71: Session:12 PATH VECTOR ROUTING
Path vector routing is similar to distance vector routing. There is at least one node, called the speaker node, in each AS that creates a routing table and advertises it to speaker nodes in the neighboring ASs..
The topics discussed in this section include:
Initialization Sharing Updating

## Slide 72: Path Vector Routing
Why distance vector routing and link state routing are not good candidates for interdomain routing?
Mostly because of scalability
  Intractable when the domain of operation becomes large

## Slide 73: Path Vector Routing (Cont.)
Distance vector routing
  Unstable if there is more than a few hops in the domain
Link state routing
  An internet is usually too big for this routing method
    Need a huge amount of resources to calculate routing table
    Create heavy traffic because of flooding
Solution
  Path vector routing

## Slide 74: Path Vector Routing (Cont.)
There is one node in each AS to act on behalf of the entire AS
  Called it speaker node
The speaker node in an AS
  Creates a routing table
  Advertises the routing table to speaker nodes in the neighboring ASs

## Slide 75: Path Vector Routing (Cont.)
Similar to distance vector routing
  Except, only speaker nodes in each AS can communicate with each other
  Furthermore, a speaker node advertises the path
 Not the metric of the nodes

## Slide 76: Initialization
At the beginning, each speaker node can know only the reachability of nodes inside its AS
A speaker in an AS share its table with immediate neighbors
When a speaker node receives a two-column tables, update its table
Add the nodes that are not in its routing table
Add its own AS and AS that sent the table

## Slide 77: Loop Prevention
Path vector routing can avoid the instability of distance vector routing and the creation of loops
When a router receives a message
  Check if its AS is in the path list
  If yes, looping is involved
 Drop the message

## Slide 78: Policy Routing
Policy routing can be easily implemented through path vector routing
  Path vector routing lists all the ASs of each path
  Once a router receives a message, it can check the path.
  If one of the AS listed in the path is against its policy,
    It can ignore that path and that destination
      Does not update its routing table with this path
      Does not send this message to its neighbors
Thus, path vector routing are not based on the
smallest hop count or the minimum metric
  Based on the policy imposed on the router by the administrator

## Slide 79: Optimum Path
The optimum path is the path that fits the organization
  Criteria may be: hop count, security and safety, reliability
Path vector routing can achieve optimum path by looking for a path best for the organization
  Since all the AS are listed in the path

## Slide 80: Session -13_BGP
Border Gateway Protocol (BGP) is an interdomain routing protocol using path vector routing. It first appeared in 1989 and has gone through four versions.
The topics discussed in this section include: Types of Autonomous Systems
Path Attributes BGP Sessions
External and Internal BGP Types of Packets
Packet Format Encapsulation

## Slide 81: BGP
BGP: Border Gateway Protocol
An inter-autonomous system routing protocol
Based on the path vector routing method

## Slide 82: Types of Autonomous Systems
The Internet is divided into hierarchical domains called autonomous systems (ASs)
  A large corporation manages its own network is an AS
AS can be classified into three categories
  Stub
  Multihomed
  Transit

## Slide 83: Stub AS
Has only one connection to another AS
Interdomain data traffic in a stub AS can be either created or terminated
  Cannot pass through a stub AS
A stub AS is either a source or a sink
Example
  A small corporation or a small ISP

## Slide 84: Multihomed AS
Has more than one connection to another AS
But it is still only a source or sink for data traffic
  There is not transient traffic
  Does not allow data coming from one AS and going to another AS to pass through
Example
  A large corporation connected to more than one regional AS but does not allow transient traffic

## Slide 85: Transit AS
A multihomed AS and allow transient traffic
Example
  National and international ISPs

## Slide 86: CIDR
BGP supports Classless Interdomain Routing addresses
The address and the prefix length are used in updating message

## Slide 87: Path Attributes
In general, the path is presented as a list of AS
Actually, the path is presented as a list of attributes
  The list of attributes help the receiving router make a better decision when applying its policy

## Slide 88: Path Attributes (Cont.)
Attributes are divided into two categories: well-known and
optional
Well-known: one that every BGP router should recognize
  Mandatory: must appear in the description of a route
    e.g., ORIGIN: the source of the routing information (RIP or OSPF)
    e.g., AS_PATH: the list of AS through which the destination can be reached
    e.g., NEXT_HOP: the next router to which data packet should be sent
  Discretionary
    Must be recognized by each router
    But is not required to be included in every update message

## Slide 89: Path Attributes (Cont.)
Optional: one that need not be recognized by every router
  Transitive
    Must be passed to the next router by the router that has not implemented this attribute
  Nontransitive
    One that should be discarded if the receiving router has not implemented it

## Slide 90: BGP Sessions
A session is a connection that is established between two BGP routers only for exchanging routing information
  Use TCP for its reliable environment
Note, a BGP session can last for a long time until something unusual happens
  BGP session thus also called semi-permanent connections

## Slide 91: External and Internal BGP Sessions
BGP have two types of sessions
  External BGP (E-BGP)
  Internal BGP (I-BGP)
E-BGP
  Exchange information between two speaker nodes belonging to two different ASs
I-BGP
  Exchange information between two routers inside an AS

## Slide 92
Figure :Internal and external BGP sessions
AS1 and AS2: E-BGP
I-BGP: collect information from other routers in their AS

## Slide 93: Types of Packets
BGP uses four different types of messages
  Open
  Update
  Keepalive
  Notification

## Slide 94: Types of BGP Messages
F
igure 13-51

## Slide 95: Packet Format
All BGP packets share the same common header
Header format
  Marker: 16-bytes
    Reserved for authentication
  Length: 2-bytes
    Define the length of the total message, including the header
  Type: 1-byte
    Define the type of the packet

## Slide 96: BGP Packet Header
F
igure 13-52 | 

## Slide 97: Open Message
Used to create a neighborhood relationship
A router running BGP opens a TCP connection with a neighbor and sends an open message
If the neighbor accepts
  It responses with a keepalive message
  The relationship then has been established between the two router

## Slide 98: Open Message
F
igure 13-53

## Slide 99: Open Message Packet Format
Version: 1-byte
  Define the version of BGP. The current version is 4
My autonomous system: 2-byte
  Define the autonomous system number
Hold time: 2-byte
  Define the maximum number of seconds that can elapsed before one of the parties receives a keepalive or update message from the other
  If a router does not receive one of the messages during the hold period, it considers the other party dead

## Slide 100: Open Message Packet Format (Cont.)
BGP number: 4-byte
  Define the router that sends the open message
Option parameter length: 1-byte
  Define the length of the total option parameters
 Since open message may also contain some option parameters
Option parameters
  The only option parameters defined so far is
authentication

## Slide 101: Update Message
Used by a router to
  Withdraw destination(route) that have advertised previously
  Announce a route to a new destination
Note, a router can withdraw several destinations in a single update message
  However, it can only advertise one new destination in a single update message

## Slide 102: Update Message Format
Unfeasible routes length: 2-byte
  Define the length of the next field
Withdraw routes
  List all routes that should be deleted from the previously advertised list
Path attributes length: 2-byte
  Define the length of the next field
Path attributes:
  Defines the attributes of the path (route) to the network
whose reachability is being announced in this msssage

## Slide 103: Update Message
F
igure 13-54

## Slide 104: Update Message Format
Network Layer reachability information (NLRI)
  Define the network that is actually advertised by this message
  Has two fields
    Length: define the number of bits in the prefix
    IP address prefix: the common part of the network address
    Example: if a network is 153.18.7.0/24
      Length = 24
      IP address prefix = 153.18.7
Thus, BGP4 supports classless addressing and CIDR

## Slide 105: Keepalive Message
The BGP routers exchange keepalive message
regularly
  Tell each other that they are alive
Format
  Consist of only the common header
Keepalive Message

## Slide 106: Notification Message
Sent by a router
  Whenever an error condition is detected
  A router wants to close the connection
Format
  Error code: 1-byte, define the category of the error
    Message header error
    Open message error
    Update message error
    Hold timer expired
    Finite state machine error
    Cease
  Error subcode: 1-byte
    Furthermore define the type of error in each category
  Error data
    Used to give more diagnostic information about the error

## Slide 107: Notification Message
F
igure 13-56 | 

## Slide 108: Table Error codes

## Slide 109: Encapsulation
BGP message are encapsulated in TCP segments using the well-known port 179
  No need for error control and flow control
Thus, when a TCP connection is opened
  The exchange of update, keepalive, and notification message is continued
  Until a notification message of type cease is sent