## Slide 1: MAGNETRON OSCILLATORS

## Slide 2: Microwave Crossed-Field Tubes (M Type)

## Slide 3: MAGNETRON OSCILLATORS
Hull invented the magnetron in 1921, but it was only an interesting laboratory device until about 1940.
All magnetrons consist of some form of anode and cathode operated in a dc magnetic field normal to a dc electric field between the cathode and anode.
Because of the crossed field between the cathode and anode, the electrons emitted from the cathode are influenced by the crossed field to move in curved paths.
If the dc magnetic field is strong enough, the electrons will not arrive in the anode but return instead to the cathode. Consequently, the anode current is cut off.

## Slide 4: Magnetrons types
Magnetrons can be classified into three types
1.Split-anode magnetron: This type of magnetron uses a static negative
resistance between two anode segments.
2. Cyclotron-frequency magnetrons: This type operates under the influence of synchronism between an alternating component of electric field and a periodic oscillation of electrons in a direction parallel to the field.
3. Traveling-wave magnetrons: This type depends on the interaction of electrons with a traveling electromagnetic field of linear velocity. They are customarily referred to simply as magnetrons.

## Slide 5: Cylindrical Magnetron
A schematic diagram of a cylindrical magnetron oscillator is shown in Fig.
This type of magnetron is also called a conventional magnetron.
In a cylindrical magnetron, several reentrant cavities are connected to the gaps. The dc voltage V0 is applied between the cathode and the anode.
The magnetic flux density B0 is in the positive z direction. When the dc voltage and the magnetic flux are adjusted properly, the electrons will follow cycloidal paths in the cathode- anode space under the combined force of both electric and magnetic fields.

## Slide 6: Equations of electron motion
The equations of motion for electrons in a cylindrical magnetron can be written as
where e/m=1.759 x 1011 C/kg is the charge-to-mass ratio of the electron,
B0 =Bz is assumed in the positive z direction.
Rearrangement of Eq. (10-1-2) results in the following form

## Slide 7: Equations of electron motion
where ωc = (e/m)Bz is the cyclotron angular frequency. Integration of Eq. (10-1-3) yields
at r = a, where a is the radius of the cathode cylinder, and dØ /dt =0, constant =-1/2 ωc a2 The angular velocity is expressed by
Since the magnetic field does no work on the electrons, the kinetic energy of the electron is given by

## Slide 8: Equations of electron motion
However, the electron velocity has r and Ø components such as
at r = b, where b is the radius from the center of the cathode to the edge of the anode, V =V0, and dr/dt =0, when the electrons just graze the anode, Eqs. (10-1-5) and (10-1-7) become
Substitution of Eq. (10-1-8) into Eq. (10-1-9) results in

## Slide 9: Equations of electron motion
The electron will acquire a tangential as well as a radial velocity. Whether the electron will just graze the anode and return toward the cathode depends on the relative magnitudes of V0 and B0.
The Hull cutoff magnetic equation is obtained from Eq.(10-1-10) as
This means that if B0 > Boc for a given V0, the electrons will not reach the anode. Conversely, the cutoff voltage is given by
This means that if V0 < V0c for a given B0, the electrons will not reach the anode. Equation (10-1-12) is often called the Hull cutoff voltage equation.

## Slide 10: Problem in Magnetron